## Slide 1: Chapter3 Filtering & Enhancing Images
图像增强基本概念
图像增强的基本方法：点方法，模板法，直方图变换
  点方法特点及典型方法
  模板法特点及典型方法：平滑和锐化
  直方图的概念及特点，直方图均衡化原理，缺点及其改进
图像增强的应用

## Slide 2
Chapter 3: Filtering & Enhancing Images
This chapter is about image processing, since the methods take an input image and create another image as output. Other appropriate terms often used are filtering, enhancement, or conditioning.
The major motion is that the image contains some signal or structure, which we want to extract, along with uninteresting or unwanted variation, which we want to suppress.

## Slide 3
(1) What Needs Enhancement?
(2) Image Enhancement in the Spatial(空间的) Domain
  Point Operation
      Linear Point Operation
      Nonlinear Point Operation
  Spatial (mask) Operation
      Noise Smoothing
      Median Filtering
      Sharping Masking
      Zooming
  Histogram Transforms
(3) Image Enhancement in the Frequency Domain Operation
Contents

## Slide 4
Before launching into the methods of this chapter, it is useful to review some of the problems that need them. Two general categories of problems follow.
  An image needs improvement (poor contrast, noise,…)
  Sharpening of image features ( such as edges or boundaries) to make a graphic display more useful for analysis.
  Low‑level features must be detected
What Needs Enhancement?

## Slide 5
Image enhancement operators improve the detectability of important image details or objects by man or machine.
  Example operations include noise reduction (smoothing), contrast stretching（拉伸）, and sharpening (edge enhancement).
  Image enhancement is subjective（主观的） (problem/application oriented)

## Slide 6: Image Enhancement - Method
Spatial Domain (image plane)
(1) Points Process: Gray level transformation
(2) Mask (Area) Process: Spatial filters
(3) Frame（框架） Process: Histogram Transforms
Frequency Domain
Combination Methods

## Slide 7: SPATIAL DOMAIN METHODS
  Transforming the pixels via a single function that maps an input gray value into a new output value
Spatial domain processes will be denoted by the expression
g(x,y)=T(f(x,y))
Where f(x,y) in the input image,g(x,y) is the processed image and T is as operator on f, defined over some neighborhood of(x,y)

## Slide 8
1 | 2 | 3 | 4 | 5 | 6
5 | 4 | 5 | 6 | 2 | 14
5/36 | 4/36 | 5/36 | 6/36 | 2/36 | 14/36
1 | 2 | 3 | 4 | 5 | 6
6 | 4 | 3 | 2 | 2 | 1
1 | 6 | 6 | 4 | 6 | 6
3 | 4 | 5 | 6 | 6 | 6
1 | 4 | 6 | 6 | 2 | 3
1 | 3 | 6 | 4 | 6 | 6
example
Histogram Transforms

## Slide 9
Question:
直方图与图像的对应关系？
一对一？ 一对多？ 多对一？ 多对对？

## Slide 10
Histogram Characteristic
The histograms of four basic types of images :
Gray level z
H(z)
Dark image
The gray levels are concentrated toward the dark end of the grayscale range. Thus this histogram corresponds to an image with overall dark characteristics.
Dark image

## Slide 11
Just is the opposite of the above.
Gray level z
H(z)
Bright image
Bright image
Histogram Characteristic

## Slide 12
Gray level z
H(z)
Low-contrast image
The histogram has a narrow shape, which indicates little dynamic range and thus corresponds to an image having low contrast.
The histogram has significant spread, corresponding to an image with high contrast.
Gray level z
H(z)
High-contrast image
Low-contrast image
High-contrast image

## Slide 13
Histogram Modification
The histogram of the “bad” image is very narrow (Fig. a), while the histogram of the “good” image is more spread (Fig. b).
To change a “bad” image to the “good” image, we need modify the histogram.
Fig.a - bad image
Gray level r
Number of pixels
Gray level s
Number of pixels
Fig.b - good image
When is it necessary to modify the Histogram of an image

## Slide 14
1
1
0
1
0
Histogram equalization（直方图均衡化） is an important method in histogram modification.
Histogram Equalization
Histogram equalization is often tried to enhance an image.
Notes: 变化后灰度级具有均匀概率密度分布

## Slide 15
Example-method1

## Slide 16
16
f(x,y):300*100
s(0)=1000/3000
s(64)=1000/3000
s(255)=1000/3000
Example-method1

## Slide 17
17
s(0)=1/3
s(64)=s(0)+s(64)=2/3
s(255)=1
T(0)=1/3*255=85
T(64)=2/3*255=170
T(255)=1*255=255
Results of histogram equalization and his histogram

## Slide 18
Method 2:

## Slide 19
Note:
(1) re-quantization method is arbitrary
(2) may not get a 1-1 mapping ⇒ inverse problem
(3) may not get a flat(平的) histogram unless L is large
Adv
这种方法对于背景和前景都太亮或者太暗的图像非常有用，这种方法尤其是可以带来X光图像中更好的骨骼结构显示以及曝光过度或者曝光不足照片中更好的细节。这种方法的一个主要优势是它是一个相当直观的技术并且是可逆操作，如果已知均衡化函数，那么就可以恢复原始的直方图，并且计算量也不大
Notes: 变换后灰度级减少，即“简并”现象

## Slide 20
The Drawback of Histogram Equalization
可能会增加背景杂讯的对比度并且降低有用信号的对比度；变换后图像的灰度级减少，某些细节消失；某些图像，如直方图有高峰，经处理后对比度不自然的过分增强。

## Slide 21
Histogram Matching(Specification)
It is not useful sometimes to enhancing image used histogram equalization.
The method used to generate a processed image that has a specified histogram is called histogram matching.
Continuous gray levels r and z.

## Slide 22
Points Process
Definition - A point operator applied to an image is an operator in which the output pixel is determined only by the input pixel, namely,point by point operation.
Out[x, y] = f (In[x, y]);
100 | 8 | 6
16 | 20 | 10
50
4
3
Operator:(Div.by 2)

## Slide 23
Methods
  Linear transformation
  Nonlinear transformation
Out[x, y] = f (In[x, y]);
Points Operation

## Slide 24
Linear transformation
Points Operation
0
f(x,y)
g(x,y)
a
b
c
d
0
f(x,y)
g(x,y)
b
d
a=0 and c=0

## Slide 25
主要用于爆光不足或过度时，改善图片质量层次不明，模糊问题
Notes: 主要用于爆光不足或过度时，改善图片质量层次不明，模糊问题

## Slide 26
Contrast stretching
Remapping the gray values is often called stretching, and which is a simple image enhancement technique that improves the contrast.
A contrast s tretching operator is a point operator that uses a piecewise smooth function f (In[x, y]) to enhance important details of the image.
255
255
142
255
255
218
48
Contrast stretch
Contrast compression

## Slide 27
Piecesise-Linear transformation
0
f(x,y)
g(x,y)
a
b
c
d
Mf
Mg

## Slide 28
28
With background:
Without background:
Intensity Level Slicing 灰度级切片

## Slide 29: Intensity Level Slicing
29
Fully illuminates pixels lying in the interval [a,b] and removes the background.
Segmentation of certain gray level region
e.g. Image from remote sensing.

## Slide 30
Using (a) transformation

## Slide 31
31
Logic operations:
NOT, AND, OR, XOR
NOT:
Create digital negative of images
Display of medical images
IMAGE NEGATIVES

## Slide 32
32
Output image
Input image
Mapping function (Reverse)
f(x)=x -1
gin
gout
0
255
255

## Slide 33
Linear transformation

## Slide 34
34
Power-Law Transformations
r<1: map a wider range of input values into a narrow range of output values, image brighter
r>1: map a narrow range of input values into a wider ranger of output values, image darkening

## Slide 36
36
Subtraction:C(x,y)=A(x,y)-B(x,y)
  Object detection: the difference between two images

## Slide 37
The least used method.
Generate the extreme range of values.
Multiplication: C(x,y)=A(x,y)×B(x,y)

## Slide 39
division: C(x,y)=A(x,y)/B(x,y)
可以用来纠正由于照明或传感器的非均匀性造成的图像灰度阴影，还被用于产生比率图像。
Notes: 避免除以0

## Slide 41
41
AND:

## Slide 43
43
OR:

## Slide 45
XOR:

## Slide 46
g(0,0)=100*3+101*2+96*2+106*1
g(0,1)=100*2+101*3+98*2+
96*1+106*2+103*1
Example

## Slide 47
At the edges of an image we are missing pixels to form a neighborhood.
Solutions?

## Slide 48
Discard the problem pixels (e.g. 512x512 input 510x510 output if mask size is 3x3)
Padding the image
  adding rows and columns of 0
  replicating rows or columns

## Slide 49
Image Smoothing
Often, an image is composed of some underlying ideal structure, which we want to detect and describe, together with some random noise or artifact, which we would like to remove.
Image contains both Gaussian noise and bright ring artifacts
Image with random noise
Scratches
Image contains artifacts

## Slide 50
Box Filter (Averaging filter)
Definition : Smoothing an image by equally weighting a rectangular neighborhood of pixels is called using a box filter.
Output-Image [r,c] = Average of some neighborhood of
Input-Image [r,c]
Example: 55 Neighborhood Filter - averages 25 pixel values in a 55 neighborhood of the input image pixel in order to create a smoothed output image.

## Slide 52
Definition : When a Gaussian filter is used, pixel [x,y] is weighted according to
x
Gaussian Filter
d is the distance of the neighborhood pixel [x, y] from the center pixel [xc, yc] of the output image where the filter is being applied.
[xc]
g(x)
[x]
d
[x]
Rather than weight all input pixels equally, it is better to reduce the weight of the input pixels with increasing distance from the center pixel I[xc, yc]. The Gaussian filter does this and is perhaps the most commonly used of all filters.
Notes: σ为函数的宽度参数 , 控制了函数的径向作用范围

## Slide 53
G77=
55
55
70
70
70
90
55
55
70
26
26
33
26
12
33
26
26
12
33
26
12
26
26
12
33
7
7
3
3
9
9
3
1
7
7
1
3
9
3
1
7
7
1
3
7
7
3
3
9
A 77 mask approximating a Gaussian with  = 2 obtained by using
to generate function values for integers x and y and then setting c = 90 so that the smallest mask element is 1.
2D Representation
3D Representation
距离,中心为（0，0）
Int(Exp(-(1+0)/8)*90)=70
Int(Exp(-(2+2)/8)*90)=55

## Slide 54
Example

## Slide 55
How to set sigma?
Depend on application
Common strategy: proportional(相称的) to image size

## Slide 56
Weights independent of spatial location
Does smooth images
But smoothes too much, and edges are blurred.
Properties of Gaussian blur

## Slide 57
Nonlinear filter-bilateral Filtering
Bilateral ﬁltering is a technique to smooth images while preserving edges
Bilateral filter: combined domain and range filtering
Reference：
1. C Tomasi, R Manduchi.Bilateral Filtering for Gray and Color Images, Computer Vision, 1998.
d(i,j,k,l)
r(i,j,k,l)
空域信息（domain）和值域信息（range）

## Slide 60
How to Set the Parameters
Depends on the application.
For instance:
• space parameter: proportional to image size
– e.g., 2% of image diagonal
• range parameter: proportional to edge amplitude
– e.g., mean or median of image gradients

## Slide 61
The presence of single dark pixels in bright regions, or single bright pixels in dark regions, is called salt‑and‑pepper noise.
Often, salt‑and‑pepper noise is the natural result of creating a binary image via thresholding.
  Salt corresponds to pixels in a dark region that somehow passed the threshold for bright.
  Pepper corresponds to pixels in a bright region that were below threshold for dark.
Removal of Salt-and-Pepper Noise (Binary Image)
Gray level z
H(z)
Salt
Pepper

## Slide 62
Binary image of bacteria
Salt‑and‑pepper noise removed using 8‑neighbors
Pepper noise removed using 8‑neighbors
Salt noise removed using 8‑neighbors
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Pepper noise
Salt noise
Removal of Salt-and-Pepper Noise by Mask

## Slide 63
Binary image of bacteria
Salt‑and‑pepper noise removed using 4‑neighbors
Pepper noise removed using 4‑neighbors
Salt noise removed using 4‑neighbors
1
1
0
1
1
1
1
1
1
1
0
0
1
0
0
0
0
0
0
0
Pepper noise
Salt noise
Removal of Salt-and-Pepper Noise by Mask

## Slide 64
Nonlinear filter-Median Filtering
Definition --- Let A[i] i = 0, 1, …(n-1) be a sorted array of n real numbers. The median of the set of numbers in A is A[(n ‑ 1)/2]
For odd n, the array has a unique middle as defined above.
If n is even, then we can define that there are two medians, at A[n/2] and A[n/2 ‑ 1], or one median, which is the average of these two values, namely:
    A[n/2] = Median value g1
    A[n/2 ‑ 1] = Median value g2
    Median value (g1 + g2)/2
In Median Filter, a pixel value is replaced with the median value of the neighborhood.

## Slide 65
Example
80
9
12
30
80
8
13
3
18
0
80
30
8
20
80
30
40
3
40
40
50
5
0
20
40
80
9
12
30
80
8
13
3
18
0
80
30
8
20
80
30
40
3
40
40
50
5
0
20
40
13
A[(n-1)/2] = A[(13-1)/2] = A[6] = 13
A[i] = 0, 3, 5, 8, 9, 12, 13, 18, 20, 30, 40, 50, 80
i = 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12

## Slide 66
Computing the median requires more computation time than computing a neighborhood average, since the neighborhood values must be partially sorted.
Moreover, median filtering is not so easily implemented in special hardware that might be necessary for real‑time processing, such as in a video pipeline.
However, in many image analysis tasks, its value in image enhancement is worth the time spent.

## Slide 67
Nonlinear filter-Rank-order Filtering
Elements under the mask are ordered, and a particular value is returned.
instance : median filter, max filter, min filter
g=ordfilt2(f, order, domain)
e.g.
min filter: g=ordfilt2(f,1,ones(m,n))
Max filter g=ordfilt2(f,m*n,ones(m,n))

## Slide 68: Magnification of Image (Zoom)
68
(a) Replication（最近邻插值）
Zero Order Hold: each pixel along a scan line id repeated once, and each scan line is repeated.
For an image, interlace it by rows and columns of zero to get a matrix, then convolve with

## Slide 69: Magnification of Image (Zoom)
69
Zooming by replication from 128×128 to 256 ×256 and 512× 512 images

## Slide 70
70
(b) Linear Interpolation
  First Order Hold-straight line fitted between pixels along row, then column.
  Can also be obtained by interlacing the image by rows and columns of zero, and then convolve with

## Slide 71
71
Zooming by linear interpolation from
128 ×128 to 256 × 256 and 512 × 512 images